## Slide 1
STOP MAKE A CHANGE 2023 – Stored Energy
Stored energy can be mechanical, gravitational, hydraulic, chemical, or pneumatic and refers to the energy stored in machines and equipment.
Stored energy hazards exist because stored energy can be released accidentally and potentially cause serious injury or even a fatality.

## Slide 2
STOP MAKE A CHANGE 2023 – Stored Energy
Where is Stored Energy found?
Mechanical – energy is contained in an item under tension. A coiled or compressed spring will release stored energy in the form of fast movement when the spring expands.
Hydraulic – energy is stored within liquid that is pressurized by an outside source. When under pressure, the fluid can be used to move heavy objects, machinery, or equipment. Examples: excavators, dumpers, concrete pumps, vehicle braking systems.

## Slide 3
STOP MAKE A CHANGE 2023 – Stored Energy
Where is Stored Energy found?
Pneumatic – energy is stored within pressurized air. Air under pressure, can be used to move heavy objects and power equipment. Examples: spraying devices, air hoses, air compressors, or air cylinders.
Gravitational - energy related to the mass of an object and its distance from the ground when it is put in motion. The heavier the object, and the further it is from the ground, the greater its gravitational energy. For example, a 5kg load falling from a crane 6 metres above the ground has greater gravitational energy than the same load falling from 4 metres.

## Slide 4
STOP MAKE A CHANGE 2023 – Stored Energy
Useful Toolbox Talks Topics
Energy sources
It is easy to overlook an energy source. Not all energy sources are obvious. Use proper lockout/tagout (LOTO)* procedures as required. Failure to follow these procedures may result in loss of life.
Electricity is not the only energy source you must account for. Do not limit your investigation to the electrical installation.
Other energy sources that can cause personal injury: mechanical (springs), hydraulic (fluids under pressure), pneumatic (air systems), chemical, and thermal.
The failure to properly lockout and tag equipment may result in debilitating injuries. It may cause you or others to lose hearing, sight, limbs, or life.
*See separate Presentation Slides on LOTO

## Slide 5
STOP MAKE A CHANGE 2023 – Stored Energy
Useful Links (highlight, then ‘Open’)
https://uk-bar.org/uploads/documents/originals/The_Safe_Off_Loading_of_Fabric.pdf
Safe Off-loading of reinforcement fabric
https://www.uk-bar.org/uploads/documents/originals/29739%20Safe-Offloading%20of%20Cut%20and%20Bent%20A5%20FINAL.pdf?randNo=4972
Safe Off-loading of cut & bent reinforcement
Safety in the storage and handling of steel and other metal stock
https://www.hse.gov.uk/pubns/books/hsg246.htm
Materials storage and waste management
https://www.hse.gov.uk/construction/safetytopics/storage.htm
https://polydrainage.co.uk/how-to-install-ducting-in-the-correct-way-2/
How to Install Ducting the Correct Way